## Slide 1: Environmental Processes Partitioning of pollutants 3.i
Sorption involving organic matter (between air/soil and water/soil)

## Slide 2
Aims:
  to provide overview of molecular interactions that govern phase transfer processes in the environment
  to discuss partitioning behavior of a compound in the environment
Outcomes:
  students will be able to evaluate compound partitioning between water, dissolved organic matter, and sediment organic matter based on physico-chemical properties of compounds
  students will be able to estimate partition constants on the basis of compound's chemical structure and physico-chemical properties

## Slide 3
Adsorption vs. Absorption: The difference between adsorption and absorption is that adsorption is the attraction between the outer surface of a solid particle and a contaminant, whereas absorption is the uptake of the contaminant into the physical structure of the solid.
Identical molecules behave very differently, depending on whether they are:
in the gas phase (gas),
surrounded by water molecules (dissolved),
clinging onto the exterior of solids (adsorbed),
buried within a solid matrix (absorbed).

## Slide 4: sorption affects transport:
generally, molecules which are sorbed are less mobile in the environment
sorbed molecules are not available for phase transfer processes (air-water exchange, etc)
and degradation:
sorbed molecules are not bioavailable
sorbed molecules usually shielded from UV light (less direct photolysis)
sorbed molecules cannot come into contact with indirect photoxidants such as OH
rates of other transformation reactions may be very different for sorbed molecules

## Slide 5
Air
Water
Octanol
A gas is a gas
T, P
Fresh, salt, ground, pore
T, salinity, cosolvents
NOM, biological lipids, other solvents
T, chemical composition
Pure Phase
(l) or (s)
Ideal behavior
PoL
Csatw
Csato
KH = PoL/Csatw
Koa
KH
Kow = Csato/Csatw
Kow
Koa = Csato/PoL

## Slide 9: Kow octanol-water partition coefficient
Kow coefficient provides a relatively convenient means of predicting the partitioning behaviour of a hydrophobic organic substance between being dissolved in water and being sorbed by solid organic matter associated with water
Kow = Co/Caq
Co – equilibrium molar solubility of the solute in octanol
Caq – equilibrium molar solubility of the solute in water

## Slide 10: Sorption isotherms can have many shapes
linear (Kd cst)
levels off at max value
mixed
as more is sorbed, sorption becomes less favorable
as more compound is sorbed, sorption becomes more favorable
???
the shape of the isotherm must be consistent with the mechanism of sorption
BUT the shape of the isotherm alone does not prove which sorption mechanism is operating

## Slide 11: The complex nature of Kd
The apparent distribution of a compound between water and solids (Kd) may be a result of many different types of sorption processes.
These processes include:
total amount in dissolved phase consists of neutral and ionized forms
sorption to organic carbon
adsorption to mineral surface
exchangeable adsorption of ionized form to charged surface
covalently bonded adsorption of ionized form to mineral surface
s refers to conc of suitable sites (mol/m2)

## Slide 12: Humic substances – metal ions interactions
This interactions are important in affecting the retention and mobilty of metal contaminants in soils and waters
These interactions include reactions between dissolved organic carbon (DOC) and metal ions, and complexation reactions between suspended organic matter (SOC) and metal ions, and bottom sediment and metal ions

## Slide 13: SOM – clay complexes
The types of interactions involved in SOM – clay complexes include:
  physical adsorption or interaction via van der Waals forces
  electrostatic interactions
  cation and anion bridges (clay mineral – metal – HS)
  chemical adsorption
  hydrogen bonding

## Slide 14: Retention of pesticides and other organic substances by humic substances
Pesticides have a strongly affinity for SOM and SOM is most important in pesticide retention
Factors that affect the retention of pesticides by SOM:
  number, type and accessability of functional groups
  nature of pesticides
  pH
  exchangeable cations
  moisture
  temperature
  soil component (types and quantities of clay minerals and other constituents)

## Slide 15: Literature
Schwarzenbach, R.P., Gschwend, P.M., Imboden, D.M. (2003). Environmental Organic Chemistry, 2nd Edition John Wiley and Sons, New Jersey.
Gary W. vanLoon, Stephen J. Duffy “Environmental Chemistry (a global perspective)” Oxford University Press, New York (2nd edition), 2005.
Donald L. Sparks “Environmental Soil Chemistry” Academic Press, Published 1995.
G. J. Lair, M. H. Gerzabek, G. Haberhauer, Environ Chem. Lett. (2007) 5:23–27