## Slide 1: Organic matter migration through sediments with water
4(iv)

## Slide 2: The lecture content:
- Migration as true solution of organic matter in water.
- Colloid solution.
- Migration of organic matter as droplets or globules
and as a continuous organic phase.

## Slide 3: Migration in the form of true solutions
- Bitumen is a mixture consisting mainly of hydrocarbons.
- Water, as very polar, is a poor solvent of the compounds of this type.
- Lower hydrocarbons can be partly dissolved, but the solubility is considerably lower when it comes to alkanes with more than 20 C-atoms.

## Slide 4: Migration in the form of true solutions
- Bitumen contains some polar compounds with nitrogen, sulphur and oxygen (NSO-compounds), which are much better soluble in water.
- Amount of NSO-compounds is much lower than the amount of hydrocarbons, which account for about 95%, so that they cannot be expected to contribute significantly to the overall solubility of total bitumen in water.
- Organic-geochemical studies have shown that oil in a reservoir rock contains a significant amount of higher n-alkanes, C23-C31, hardly soluble in water, compared to bitumen in the source rock.

## Slide 5: Migration in the form of true solutions
- The migration mechanism in the form of true solutions cannot be the dominant mechanism of bitumen migration.
- Still, it would be wrong to exclude this mechanism completely.
- True solutions in migration could be of greater importance in areas characterized by narrow passages, i.e. small diameters of fractures and pores.

## Slide 6: Migration in the form of colloid solution
- The fact that oil in a reservoir rock often contains a significant amount of higher normal alkanes (> C20) compared to bitumen in a source rock, is not logical at first sight, not only because the higher n-alkanes are hardly soluble in water, but because of the fact that during the migration heavier (and polar) compounds are left behind. According to that, the amount of lower n-alkanes in oil should be higher.
- This apparent contradiction may be explained by the fact that NSO-compounds form colloidal micelles in water, which include only n-alkanes, especially the higher ones, thus transporting them to the reservoir rock.
- So, one of possible mechanisms of bitumen migration through sediments may be in the form of colloidal micelles. It is hard to believe that there are environments in which this mechanism is dominant. However, in this case it would be wrong to exclude it completely.

## Slide 7: Migration of organic matter as droplets or globules, and as a continuous organic phase
- The secondary migration of bitumen, through a much more permeable environment compared to that characteristic of the primary migration, takes place mainly through pores or fractures.
- It is possible that the bitumen moves by simply "floating" on the water surface.
- Depending on the size of these pathways, small aggregates in the form of globules or droplets can be formed on the water surface, or they can be considerably higher, in the form of a continuous phase. In such cases, the interaction between bitumen and water is relatively poor and water does not significantly affect the composition of the bitumen.

## Slide 8
During migration, various changes in the composition of bitumen take place, so that the chemical composition of oil can vary significantly from the bitumen of the source rock. These changes are the result of heavier compounds being left behind or interaction between polar, NSO-compounds, and the inorganic environment. What is the intensity of these interactions depends on the length of the migration pathway, but also the physical and geological properties of sedimentary formation through which bitumen migrates.