## Slide 1: Petroleum transformations
5(ii)

## Slide 2: The lecture content:
- Petroleum transformation in reservoir rocks (as a native matter).
- Petroleum transformation in the environment (as an anthropogenic matter).

## Slide 3: Reservoir rocks
A simplified illustration of the oil reservoir rock.

## Slide 4
Accumulation is the collection process of bitumen in tight reservoir rocks – the end of migration
- The temperature pressures in reservor rocks are generally lower.
- The contact of oil with inorganic environment in the reservoirs is weaker.
- Further changes in the composition of oil still take place in the reservoir rocks:
1) maturation changes,
2) deasphalting process,
3) water washing and
4) biodegradation.

## Slide 5: 1) Maturation changes
- Regardless of the slightly lower temperatures and pressures and a weaker contact with potential mineral catalysts, all the maturation processes which took place in bitumen are continued in the oil reservoir rocks, which leads to the increased amounts of low molecular weight compounds, and thermodynamically more stable structural and stereochemical isomers of certain compounds.

## Slide 6
- All maturation changes of n-alkanes, isoprenoid aliphatic alkanes, polycyclic alkanes and naphthenic aromatic compounds are continued, if an equilibrium state has not already been reached in the "bituminous stage“.
The equilibrium values of most important maturation parameters (n-alkanes, terpanes and steranes) and the corresponding values of vitrinite reflectance (Rr)

## Slide 7: 2) Deasphalting process
The part of asphaltene structure.

## Slide 8: Deasphalting process
- Since the amount of lower hydrocarbons increases during the cracking, including pentane, hexane and heptane, which are excellent solvents for the whole oil, except for asphaltene, deasphalting takes place, i.e. precipitation of asphaltenes in reservoir rocks, and thus the contents of compounds soluble in alkane solvents, saturated and aromatic hydrocarbons and NSO-compounds increases.
- In organic geochemistry, these three fractions are often collectively referred to as "maltenes".
- In addition to asphaltenes and maltenes, oil contains also "volatile components". These are hydrocarbons with less than 12 C-atoms. They mostly "evaporate" during the laboratory investigations of oil, since most analytical methods include experiments at elevated temperatures.

## Slide 9: 3) Water washing
- Water plays a crucial role in the transmission of the bitumen from source to reservoir rocks. Therefore, water and above it oil, as it has lower specific gravity, are accumulated together in the reservoir.
- In the reservoir rocks, oil is in constant contact with water and therefore in a long geologic time, it is subject to continuous water washing.
- Oil is, as a mixture of nonpolar hydrocarbons, poorly soluble in water. However, it also contains some compounds that are soluble in water, especially at higher temperatures and pressures. This is primarily about compounds with heteroatoms, nitrogen, sulphur and oxygen, forming the so-called NSO-fraction. Therefore water washing is mostly "washing" of NSO-compounds, which of course does not mean that some low molecular weight hydrocarbons cannot be "washed", although to much lesser extent.

## Slide 10: 4) Biodegradation
- Biodegradation (microbiological degradation) is the process that can largely alter the composition of oil in the reservoir rocks.
- It occurs only in reservoir rocks that contain water as well.
- Biodegradation is possible only in reservoir rocks with the temperature below 66 degrees.

## Slide 11
Petroleum transformation from
paraffinic type to naphthenic and aromatic type:
A good process from the technical
and technological aspects
(Naphthenic oil is a better raw material for producing high quality gasoline )
Undesirable process from organic-geochemical,
fundamental, aspect
(Degradation of biological markers as a tool for assessing the origin and geological history of oil)

## Slide 12: The classification of crude oils based on the degree of biodegradation (1983)
1. No
2. The lower n-alkanes ………….. minimum of biodegradation
3. More than 99% of n-alkanes ………………….. moderate (I)
4. Alkylcyclohexanes; partially isoprenoids ……..moderate (II)
5. All isoprenoids ………………………………. moderate (III)
6. Bicyclic alkanes ……………………………..medium strong
7. More than 50% of regular steranes ………………….. strong
8. Steranes changed, a lot of demethylated hopanes very strong
9. All regular steranes, domination of diasteranes and demethylated hopanes ………………..……... the maximum

## Slide 13
Schematic diagram of physical and chemical changes
occurring during crude oil and natural gas biodegradation (2003).

## Slide 14
TICs showing aliphatic and aromatic hydrocarbon distributions in oils
(collected from reservoirs) at various levels of biodegradation (Huang et al., 2004).
MN – methylnaphthalenes; DMN – dimethylnaphthalenes; TMN – trimethylnaphthalenes;
TEMN – tetramethylnaphthalenes; P – phenanthrene; MP – methylphenanthrenes;
DMP – dimethylphenanthrenes; MAS – monoaromatic steroid hydrocarbons;
TAS – triaromatic steroid hydrocarbons; MTAS – methyl triaromatic steroid hydrocarbons

## Slide 15
Biodegradation of naphthalene (N), methylnaphthalenes (MN) and dimethylnaphthalenes
(DMN) in natural marine environment (coastal sediments) (2002).
Numbers designate positions of methyl group in naphthalene

## Slide 16
Biodegradation of trimethylnaphthalenes (TMNs) and tetramethylnaphthalenes (TeMNs)
in natural marine environment (coastal sediments) (2002).
Numbers designate positions of methyl group in naphthalene

## Slide 17
Biodegradation of phenanthrene (P), methylphenanthrenes (MPs) and C2 substituted
phenanthrenes (C2-PS) in natural marine environment (coastal sediments; 2002).
DMPs – dimethylphenanthrene; EP– ethylphenanthrene; Numbers designate positions of methyl group in phenanthrene

## Slide 18
Gas chromatograms of total alkane oil fractions ranked according to the intensity of biodegradation: a) non-biodegraded oil, b) at least biodegraded oil, c) moderate (I) biodegraded oil and d) moderate (III) biodegraded oil.

## Slide 19: 1) Natural biodegradation. 2) Biodegradation of the oil pollutant in the laboratory. 3) in situ Bioremediation.
BIODEGRADATION OF PETROLEUM AS POLLUTANT IN THE ENVIRONMENT – the most important type of transformations

## Slide 20
Alkanes isolated from oil polluted alluvial ground waters (Pančevo Oil Refinery locality). November 1997 (a), May 1998 (b), September 1998 (c), September 1999 (d) and February 2000 (e).
1) Natural biodegradation (example)

## Slide 21
The fate of a petroleum-type pollutant in environment was foreseen on the basis of laboratory simulation experiments of microbiological degradation of petroleum using microorganism consortiums similar to those typical for the natural environment.
2) Biodegradation of the oil pollutant in the laboratory (example)

## Slide 22
- Experiments of simulated biodegradation after 15, 30, 45, 60, and 75 days, and experiment with blind trial after 75 days, were stopped for sterilisation at 120 oC for 25 minutes.
- In the extracts, group composition was determined and fractions of saturated hydrocarbons, aromatic hydrocarbons, alcohols and fatty acids were isolated by column chromatography.
- Alkane fraction was analysed by gas chromatography - mass spectrometry (GC-MS) technique.

## Slide 23
Total ion chromatograms (TIC) of saturated fractions after the experiment
of simulated biodegradation with bacteria.
n-C35
Pr
0. day
15. day
30. day
45. day
60. day
n-C15
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
n-C20
n-C25
n-C30
75. day
n-C17
n-C18
Fit
Retention time (min)

## Slide 24
n-C35
0. day
15. day
30. day
45. day
60. day
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
75. day
n-C15
n-C20
n-C25
n-C30
n-C17
n-C18
Pr
Fit
Retention time (min)
Total ion chromatograms (TIC) of saturated fractions after the
experiment of simulated biodegradation with fungi.

## Slide 25
0. day
15. day
30. day
45. day
60. day
n-C15
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
n-C20
n-C25
n-C30
n-C35
75. day
n-C17
n-C18
Pr
Fit
Retention time (min)
Total ion chromatograms (TIC) of saturated fractions after the experiment
of simulated biodegradation with consortium of bacteria and fungi.

## Slide 26
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Retention time (min)
Retention time (min)
15. day
30. day
45. day
60. day
75. day
0. day
Terpanes
Steranes
Triciclyc
terpanes
Pentaciclyc
terpanes
C21
C20
C27
C28
C29
Diasteranes
GC-MS ion fragmentograms of steranes (m/z = 217) and terpanes (m/z = 191)
after the experiment of simulated biodegradation with consortium of bacteria and fungi.

## Slide 27
15. day
30. day
45. day
60. day
75. day
0. day
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Retention time (min)
P
MP
DMP
GC-MS ion fragmentograms of phenanthrene (P; m/z = 178), methylphenanthrenes (MP; m/z = 192) and dimethylphenanthrenes (DMP; m/z = 206) after the experiment of simulated biodegradation with bacteria.

## Slide 28
15. day
30. day
45. day
60. day
75. day
0. day
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
Retention time (min)
P
DMP
MP
GC-MS ion fragmentograms of phenanthrene (P; m/z = 178), methylphenanthrenes (MP; m/z = 192) and dimethylphenanthrenes (DMP; m/z = 206) after the experiment of simulated biodegradation with fungi.

## Slide 29
Abundance
Abundance
Abundance
Abundance
Abundance
Abundance
15. day
30. day
45. day
60. day
75. day
0. day
Retention time (min)
P
DMP
MP
GC-MS ion fragmentograms of phenanthrene (P; m/z = 178), methylphenanthrenes (MP; m/z = 192) and dimethylphenanthrenes (DMP; m/z = 206) after the experiment of simulated biodegradation with consortium of bacteria and fungi.

## Slide 30: 3) in situ Bioremediation (example)
- Ground waters (GW) which contained dissolved hydrocarbons and a floating layer of an oil pollutant were treated with filtration-adsorption remediation technique, using the columns filled with natural inorganic hydrophobic adsorbents, and in situ bioremediation based on the principle of “bipolar” model.
- In situ bio/remediation of GW and soil layers in contact with groundwater was accomplished by chemical and biological stimulation, augmentation and aeration in closed “bipolar” system (pumping out – pumping in), with adsorption in the “external unit”.
- Natural microbial processes in groundwater were additionally stimulated by chemical or physical increase in the aeration capacity.
- Bioaugmentation was achieved by injection of biomass of zymogenous microorganisms isolated from treated polluted GW.

## Slide 31
Fragmentograms of n-alkanes and isoprenoids (m/z = 71) obtained by GC-MS analysis of the extracts isolated from the samples at the beginning of the experiment, after 30 days and after 60 days.
Abundance
Abundance
n-C17
Pr
n-C18
Fit
n-C20
n-C15
n-C25
n-C30
1st May 2012
1st June 2012
Retention time (min)
Abundance
1st July 2012
in situ Bioremediation
(example)

## Slide 32
Fragmentograms of terpanes (m/z = 191) obtained by GC-MS analysis of the extracts isolated from the samples at the beginning of the experiment, after 30 days and after 60 days.
Abundance
Abundance
1st May 2012
1st June 2012
Triciclyc
terpanes
Pentaciclyc
terpanes
Retention time (min)
Abundance
1st July 2012
in situ Bioremediation

## Slide 33
Fragmentograms of steranes (m/z = 217) obtained by GC-MS analysis of the extracts isolated from the samples at the beginning of the experiment, after 30 days and after 60 days.
1st May 2012
1st June 2012
C27
C28
C29
Diasteranes
Abundance
Abundance
1st July 2012
Retention time (min)
Abundance
in situ Bioremediation

## Slide 34
Fragmentograms of phenanthrene (P; m/z = 178), methylphenanthrenes (MP; m/z = 192), dimethylphenanthrenes (DMP; m/z = 206) and trimethylphenanthrenes (TMP; m/z = 220) obtained by GC-MS analysis of the extracts isolated from the samples at the beginning of the experiment, after 30 days and after 60 days.
1st June 2012
Abundance
Abundance
P
DMP
MP
TMP
1st May 2012
Retention time (min)
1st July 2012
Abundance
in situ Bioremediation